## Slide 1: Option B :Engineering physics b.2 – Thermodynamics
Option B.2 is an extension of Topic 3.
Essential idea: The first law of thermodynamics relates the change in internal energy of a system to the energy transferred and the work done. The entropy of the universe tends to a maximum.
Nature of science: Variety of perspectives : with three alternative and equivalent statements of the second law of thermodynamics, this area of physics demonstrates the collaboration and testing involved in confirming abstract notions such as this.
Notes: © 2015 by Timothy K. Lund

## Slide 2
Understandings:
The first law of thermodynamics
The second law of thermodynamics
Entropy
Cyclic processes and pV-diagrams
Isovolumetric, isobaric, isothermal and adiabatic processes
Thermal efficiency
Option B :Engineering physics B.2 – Thermodynamics
Notes: 2
© 2015 by Timothy K. Lund

## Slide 3
Applications and skills:
Describing the first law of thermodynamics as a statement of conservation of energy
Explaining sign convention used when stating the first law of conservation of energy as Q=ΔU + W
Solving problems involving the first law of thermodynamics
Describing the nature of the exponential discharge of a capacitor second law of thermodynamics in Clausius form, Kelvin form and as a consequence of entropy
Describing examples of processes in terms of entropy change
Option B :Engineering physics B.2 – Thermodynamics
Notes: 3
© 2015 by Timothy K. Lund

## Slide 4
Applications and skills:
Solving problems involving entropy changes
Sketching and interpreting cyclic processes
Solving problems for adiabatic processes for monoatomic gases using pV5/3 = constant
Solving problems involving thermal efficiency
Option B :Engineering physics B.2 – Thermodynamics
Notes: 4
© 2015 by Timothy K. Lund

## Slide 5
Guidance:
If cycles other than the Carnot cycle are used quantitatively, full details will be provided
Only graphical analysis will be required for determination of work done on a pV diagram when pressure is not constant
Option B :Engineering physics B.2 – Thermodynamics
Notes: 5
© 2015 by Timothy K. Lund

## Slide 6
Data booklet reference:
Option B :Engineering physics B.2 – Thermodynamics
Notes: 6
© 2015 by Timothy K. Lund

## Slide 7
International-mindedness:
The development of this topic was the subject of intense debate between scientists of many countris in the 19th century.
Option B :Engineering physics B.2 – Thermodynamics
Notes: 7
© 2015 by Timothy K. Lund

## Slide 8
Utilization:
This work leads directly to the concept of the heat engines that played such a large role in modern society
The possibility of the heat death of the universe is based on ever-increasing entropy
Chemistry of entropy (see Chemistry sub-topic 15.2)
Option B :Engineering physics B.2 – Thermodynamics
Notes: 8
© 2015 by Timothy K. Lund

## Slide 9
Aims:
• Aim 5: Development of the second law demonstrates the collaboration involved in scientific pursuits
• Aim 10: The relationships and similarities between scientific disciplines are particularly apparent here
Option B :Engineering physics B.2 – Thermodynamics
Notes: 9
© 2015 by Timothy K. Lund

## Slide 10
Thermodynamics =
The study on how energy can do work
Option B :Engineering physics B.2 – Thermodynamics
Thermal energy … can produce useful work
work can produce …
Thermal energy
Notes: 10
© 2015 by Timothy K. Lund

## Slide 11
Thermodynamics =
The study on how energy can do work
Option B :Engineering physics B.2 – Thermodynamics
Thermal energy … can produce useful work
work can produce …
Thermal energy
Notes: 11
© 2015 by Timothy K. Lund

## Slide 12
Materials have internal energy U =
This is the KE of random motions of atoms + PE due to forces between atoms
Can be modeled as vibrating springs joining atoms to each other in solids or within molecules
Energy is also stored as vibrational, rotational and translational motions
Option B :Engineering physics B.2 – Thermodynamics

## Slide 13: Internal energy
Materials have internal energy U,
(thermal energy + potential energy in bonds)
U is the sum of all KE and PE of atoms/molecules in the material
U is the change of internal energy
If U > 0 then internal energy has increased
If U < 0 then internal energy has decreased
Option B :Engineering physics B.2 – Thermodynamics

## Slide 14: Internal Energy of Ideal gases
k is Boltzmann’s constant, 1.38 (10-23) J/K, T is absolute temperature
For each “degree of freedom” (different direction in 3D space) an atom (or molecule) can store energy:  kT
 U =  NkT for a monatomic gas with N molecules, since there are 3 dimensions (directions)
In an Ideal Gas U  T (in K)
In polyatomic gases the molecules can store energy in rotations, and vibrations, as well as translations and this adds more degrees of freedom increasing the internal energy at a given temperature so that complex gases are slower to warm up
Option B :Engineering physics B.2 – Thermodynamics

## Slide 15: Heat and Internal Energy
Heat is not Internal Energy
Heat is the flow of Thermal Energy from one object to another and will increase the Internal Energy of the receiver and decrease the Internal Energy of the donor
(Like Work is not Mechanical Energy,
Work is the transfer of Mechanical Energy from one object to another)
HEAT more random motion (<KE>) higher temperature
HEAT stretched bonds  higher PE, without changing T
Option B :Engineering physics B.2 – Thermodynamics

## Slide 16: Heat Engines and Refrigerators
The reasons for studying thermodynamics were mainly practical – engines and the Industrial Revolution
Efficient engines were needed which meant analyzing how fuel (thermal energy) may be harnessed to do useful work.
The earliest known engine is Hero’s – a Greek from Alexandria 2000 years ago.
Engines use a working fluid, often a gas, to create motion and drive equipment
Engines (and refrigerators) must repeat their cycles over and over to continue to do work
Option B :Engineering physics B.2 – Thermodynamics

## Slide 17: 0th Law of Thermodynamics
(this is the 0th law because it was added after 1,2, and 3)
Temperature exists and can be measured
When 2 objects are in thermal equilibrium separately with a 3rd object then they are in thermal equilibrium with each other
Thermal equilibrium means there is no net thermal energy flow between the objects
T1 = T2 and T2 = T3  T1 = T3

## Slide 18: 1st Law of Thermodynamics
Q = ΔU + W
Energy is conserved – it is neither created not destroyed
Internal energy of a system may change as any combination of
Doing work on the system
Transferring energy to or from the system as a result of a difference in temperature
When Q > 0 : energy transferred from surroundings to the system because Tsurroundings > Tsystem
ΔU >0 : increase in internal energy
W>0 : work done by system as is expands
When Q < 0 …?

## Slide 19
1000 J of thermal energy flows into a system (Q = 1000 J). At the same time, 400 J of work is done by the system (W = 400 J).What is the change in the system's internal energy U?
EXAMPLE
U = Q –W
= 1000 - 400
= 600 J
Notes: 19

## Slide 20
800 J of work is done by a system (W = 800 J) as 500 J of thermal energy is removed from the system (Q = -500 J).What is the change in the system's internal energy U?
EXAMPLE
U = Q –W
= -500 – 800
= -1300 J
NB: work done on the system is +, work done by the system is -
& heat into the system is +, heat out of the system is -
Notes: 20

## Slide 21
Considering an ideal gas enclosed in a cylinder by a moveable piston (gas = system, cylinder + piston = boundaries and walls)
A state is a unique set of values for P, V, n, & T
(so PV = nRT is also called a “State Equation”)
There are 4 basic processes with n constant
Isobaric, a change at constant pressure
Isochoric or isovolumetric, a change at constant volume, W = 0
Isothermal, a change at constant temperature (U = 0, Q = W)
Adiabatic, a change at no heat (Q = 0)
“iso” means “same”
Option B :Engineering physics B.2 – Thermodynamics
A system can change its state
Using the first law for ideal gases

## Slide 22: Option B :Engineering physics B.2 – Thermodynamics
Work done in an isobaric change
Isobaric = constant p
Gas expands : piston moves up a distance d
Volume increases ΔV = Ad
Force of the gas on piston F=pA
Work done by the gas on the surroundings : W = Fd = pAd = pΔV

## Slide 23: Option B :Engineering physics B.2 – Thermodynamics
Work done in a non-isobaric change
W = area under graph in pV-graph

## Slide 24: Option B :Engineering physics B.2 – Thermodynamics
Work done in an isothermal change
Isothermal = constant T
Internal energy = sum of mean KE of particles of gas = proportional to the temperature of the gas
IF T = constant : Internal energy of the system = constant
For Q = ΔU + W with ΔU =0 → Q = W
If Q > 0 : work done by system on surroundings → expansion of gas
If Q < 0 : work done by surroundings on system → compression of gas

## Slide 25: Option B :Engineering physics B.2 – Thermodynamics
Work done in an isovolumetric change
Isovolumetric = constant V
When V = constant then NO work can be done
For Q = ΔU + W with W =0 → Q = ΔU
If Q > 0 : increase of internal energy of system
If Q < 0 : decrease of thermal energy of system
Equation of state : p/T = constant

## Slide 26: Option B :Engineering physics B.2 – Thermodynamics
Adiabatic change
Adiabatic = no energy is transferred
When V = constant then NO work can be done
For Q = ΔU + W with W =0 → Q = ΔU
If Q > 0 : increase of internal energy of system
If Q < 0 : decrease of thermal energy of system
Equation of state : p/T = constant

## Slide 27: Option B :Engineering physics B.2 – Thermodynamics

## Slide 28: Option B :Engineering physics B.2 – Thermodynamics

## Slide 29: Option B :Engineering physics B.2 – Thermodynamics

## Slide 30: Option B :Engineering physics B.2 – Thermodynamics

## Slide 31
How much work is done by the system when the system is taken from:
(a) A to B (900 J) (b) B to C (0 J) (c) C to A (-1500 J)
EXAMPLE
Each rectangle on the graph represents 100 Pa-m³ = 100 J
(a) From A B the area is 900 J, isobaric expansion
(b) From B  C, 0, isovolumetric change of pressure
(c) From C A the area is -1500 J
Notes: 31

## Slide 32
10 grams of steam at 100 C at constant pressure rises to 110 C: P = 4 x 105 Pa T = 10 C V = 30.0 x 10-6 m3 c = 2.01 J/g
What is the change in internal energy?
EXAMPLE
U = Q – W
U = mcT – PV
U = 189 J
So heating the steam produces a higher internal energy and expansion
Notes: 32

## Slide 33
Aluminum cube of side L is heated in a chamber at atmospheric pressure. What is the change in the cube's internal energy if L = 10 cm and T = 5 °C?
EXAMPLE
U = Q – W
Q = mcT m = V0 V0 = L3 W = PV V = V0T
U = mcT – PV
U = V0cT – PV0T
U = V0T (c – P)
cAl = 0.90 J/g°C
Al = 72(10-6) °C-1
U = L³T (c – P)
Patm = 101.5 kPa
Al = 2.7 g/cm³
U = 0.10³(5)((2700)(900) – 101.5(10³)(72(10-6))
U = 12,150 J
NB: P is neglible
Notes: 33

## Slide 34
Isobar
Isochore
Isotherm
P
V
1, (P1,V1) T1
2, (P2,V2) T2
3, (P3,V3) T3
4, (P4,V4) T4
1. P2 = P1 = 1000 kPa
Isotherm
2. T4 = T1 = 400 K
3. T3 = T2 = 600 K
4. P3 = P2V2/V3 = 625 kPa
5. P4 = P1V1/V4 = 250 kPa
W = Area enclosed
= P1V12 +  (P2+P3)V23 +  (P1+P4)V41
= (15 + 12.188 – 18.75)(10³) = 8.44 kJ
Find the work done for a cycle if P1 = 1000 kPa, V1 = 0.01 m³,
V2 = 0.025 m³, V3 = V4 = 0.04 m³, T1 = 400 K, T2 = 600K, n = 2 mol
EXAMPLE
W = Area enclosed
+  (P2+P3)V23
= P1V12
–  (P1+P4)V41

## Slide 35
Isobar
Isochore
Isotherm
P
V
1, (P1,V1) T1
2, (P2,V2) T2
3, (P3,V3) T3
4, (P4,V4) T4
Find the internal energy for each state if P1 = 1000 kPa, V1 = 0.01 m³,
V2 = 0.025 m³, V3 = V4 = 0.04 m³, T1 = 400 K, T2 = 600K, n = 2 mol
1. P2 = P1 = 1000 kPa
Isotherm
2. T4 = T1 = 400 K
3. T3 = T2 = 600 K
6. U1 =  nRT1 = 9972 J
7. U4 = U1 = 9972 J
9. U3 = U2 = 14958 J
8. U2 =  nRT2 = 14958 J
4. P3 = P2V2/V3 = 625 kPa
5. P4 = P1V1/V4 = 250 kPa
EXAMPLE

## Slide 36
Isobar
Isochore
Isotherm
P
V
1, (P1,V1) T1
2, (P2,V2) T2
3, (P3,V3) T3
4, (P4,V4) T4
Find the thermal energy change Q for each state if P1 = 1000 kPa,
V1 = 0.01 m³, V2 = 0.025 m³, V3 = V4 = 0.04 m³, T1 = 400 K, T2 = 600K, n = 2 mol
1. P2 = P1 = 1000 kPa
Isotherm
2. T4 = T1 = 400 K
3. T3 = T2 = 600 K
6. U1 =  nRT1 = 9972 J
7. U4 = U1 = 9972 J
9. U3 = U2 = 14958 J
8. U2 =  nRT2 = 14958 J
10. Q12 = U12 + W12 = 34986 J
12. Q34 = U34 = -4986 J
13. Q41 = W41 (U41 = 0) W41 =  (P4+P1)V41 = - 18.75 kJ
4. P3 = P2V2/V3 = 625 kPa
5. P4 = P1V1/V4 = 250 kPa
EXAMPLE
11. Q23 = W23 (U23 = 0) W23 =  (P2+P3)V23 = 12.188 kJ
Q12
Q34
Q34
Q41

## Slide 37: 2nd Law of Thermodynamics
Clausius version :
It is impossible to transfer energy from a body at a lower temperature to one at higher temperature without doing work on the system.
Kelvin version :
It is impossible to extract energy from a hot reservoir and transfer this entirely into work
Explanation :
A hot cup of coffee gets colder after some time. We can heat it up again by transferring energy using a heating coil or by doing work on it (stirring very fast)

## Slide 38: 2nd Law of Thermodynamics
Explanation :
Internal energy of object is related with random motion of the molecules.
When we want to convert the internal energy into work we are trying to convert random motion into something more ordered : this is impossible !!!!
Explanation :
Efficiency can not =1 therefore some of the energy will always be degraded, not all the supplied energy can be converted into work.

## Slide 39: Entropy
Is a thermodynamic function of the state of the system
Can be interpreted as the amount of order or disorder of a system
As with internal energy, it is the change in entropy is important and not its absolute value.
The change in entropy S of a system = an the amount of thermal energy Q absorbed by a system divided by the (constant) absolute temperature T at which this occurs
The units of the change in entropy are JK-1

## Slide 40: 2nd Law of Thermodynamics
Consequence of entropy:
The entropy, disorder, always increases in closed systems
In closed systems, S > 0 for all real processes
Only in the ideal case of maximum efficiency would S = 0
The total entropy of the universe increases !!!
ΔSuniv = ΔSsys + ΔSsurr > 0

## Slide 41: Heat death
A final consequence of the second Law is the heat degradation of the Universe.
It can be reasoned that in any natural process, some energy becomes unavailable to do useful work.
An outcome of this suggests that the Universe will eventually reach a state of maximum disorder.
An equilibrium temperature will be reached and no work will be able to be done.
All change of state will cease as all the energy in the Universe becomes degraded to thermal energy.
This point in time is often referred to the heat death of the Universe.

## Slide 42
Consider a hypothetical device that takes 1000 J of heat from a hot reservoir at 300K, ejects 200 J of heat to a cold reservoir at 100K, and produces 800 J of work. Is this possible?
EXAMPLE
The maximum efficiency is emax = 1 – TL/TH = 67%,
but the proposed efficiency is eprop = W/QH = 80%.
This violates the 2nd law – do not buy shares in the company designing this engine!

## Slide 43
Consider a hypothetical refrigerator that takes 1000 J of heat from a cold reservoir at 100K and ejects 1200 J of heat to a hot reservoir at 300K. Is this possible?
EXAMPLE
The entropy of the cold reservoir decreases by SC = 1000 J / 100 K = 10 J/K
The entropy of the heat reservoir increases by SH = 1200 J / 300 K = 4 J/K
There would be a net decrease in entropy which would violate the 2nd Law, so this refrigerator is not possible
What is the minimum work needed?
 2000 J, so that SH becomes at least 10 J/K

## Slide 44
https://www.youtube.com/watch?v=870y6GUKbwc
https://www.youtube.com/watch?v=GOrWy_yNBvY#t=1614